## Slide 1: SMART HOME AUTOMATION SYSTEM
PRESENTED BY-
Mohd Abid

## Slide 2: PROJECT OVERVIEW
This project uses an Arduino uno to build a smart system.
Integrates multiple sensors:
Ultrasonic sensor- Measures distance.
PIR motion sensor – Detects human motion .
LDR sensor- Detects ambient light level.
Gas sensor- Monitors gas leakage.
Controls appliances and alerts:
Relay module- Controls light.
Buzzer: Alerts on high gas levels.
LCD display- Shows sensor readings.

## Slide 3: COMPONENTS USED
Arduino UNO
LCD 16x2 Display
LDR Sensor
Gas Sensor (MQ-2)
PIR Motion Sensor
Ultrasonic Sensor
Buzzer
Relay module
Power Supply
Resistor
Bulb
Dc Motor

## Slide 5: CIRCUIT DIAGRAM

## Slide 6: CODE

## Slide 8: ARDUINO CODE OVERVIEW
LDR controls a relay to switch a bulb based on light intensity
PIR sensor detects motion and controls dc motor
GAS sensor detects LPG leakage and activates a buzzer
LCD displays sensor readings and system messages

## Slide 9: LDR AND RELAY CONTROL
LDR Monitors ambient light
If light intensity <600, bulb turns OFF.
If >600, darkness bulb turns ON
LCD displays current light value and status

## Slide 10: If light intensity>600, bulb turns ON

## Slide 11: If light intensity<600, bulb turns OFF

## Slide 12: PIR MOTION DETECTION
PIR sensor detects human movement
If motion detected: MOTOR ROTATES, BULB TURNS ON
If no motion detected: MOTOR STOPS, BULB TURNS OFF

## Slide 13: WHEN MOTION DETECTED : MOTOR ROTATES, BULB TURNS ON

## Slide 14: GAS DETECTION AND ALARM
MQ-2 gas sensor detects gas concentration.
If value <=85 LCD display LOW
If value <=120 LCD display MED
If value =200 LCD display HIGH
If value <200LCD display EXT
If value above 200 then buzzer turns ON

## Slide 15: If value <=85 LCD display LOW

## Slide 16: If value <=120 LCD display MED

## Slide 17: If value <=200 LCD display HIGH

## Slide 18: CONCLUSION
Integrates various sensors and modules into a smart home model.
Helps automate lighting, security, gas leakage alert.
Ideal for low-cost ,Arduino-based home automation projects.

## Slide 19: THANK YOU